## Slide 1
1 frame = 10 subframes, 1 subframe = 1 ms = slots, 1 slot = 14 symbols
1 frame
= 10 subframes
1 ms
2 ms
3 ms
4 ms
5 ms
6 ms
7 ms
8 ms
9 ms
10 ms
= 20 slots (μ = 1)
= 280 symbols ()
1 SSB = 20 resource blocks
Frequency
Time
30 kHz = 30,000 count per second
Subcarrier spacing
1 resource block = 12 subcarriers
1 SSB
= 20 resource blocks
= 240 subcarriers ()
= 7200 kHz = 7.2 MHz ()
1 subcarrier = 30 kHz ()
SC 48
SC 24
SC 0
SC 72
SC 12
SC 36
SC 60
SC 84
SC 96
SC 108
SC 120
SC 240
SC 228
SC 216
SC 204
SC 192
SC 180
SC 168
SC 156
SC 144
SC 132
0 to 47
56 to 182
192 to 239
8
9
48
127
48
5G NR Frame Structure
SSB
Primary Synchronization Signal (PSS)
Physical Broadcast Channel (PBCH)
Physical Broadcast Channel (PBCH)
Secondary Synchronization Signal (SSS)
PBCH
PBCH
SSB
Symbol
1
2
3
4
Numerology | Slots per Subframe | Slots per Frame | Subcarrier Spacing
μ = 0 (LTE) | 1 | 10 | 15 kHz
μ = 1 | 2 | 20 | 30 kHz
μ = 2 | 4 | 40 | 60 kHz
μ = 3 | 8 | 80 | 120 kHz
μ = 4 | 16 | 160 | 240 kHz
μ = 5 | 32 | 320 | 480 kHz
One SSB every 5 ms (0.5 frames), 10 ms (1 frame), 20 ms (2 frames), 40 ms (4 frames), 80 ms (8 frames), or 160 ms (16 frames)